Model:	AL-Mini01-700

##### High resolution, 700 TVL, 12VDC, NTSC

Features:

●  Metal-cased mini housing with standard fixed lens.

●  Available in white finish.

●  Low power consumption.

●  Infrared 12 LEDs.

●  Easy installation on ceiling or wall, surface or flush mount.

Cautions:

- Please do not touch the glass. If necessary, use a soft cloth moistened with alcohol to wipe away the dust.

- Please avoid placing or using the camera under direct sunlight.

- Please ensure that the input voltage range is within the specifications.

- Do not attempt to service the camera by yourself. Please refer all services to qualified Dealers.

Packing list:

Camera	                  1

Instruction Manual	                  1

Mounting Screw	                  3

Mounting Plug	                  3

Rubber Ring	                  1

Optional Lens        selectable from f3.6mm to f12mm

Dimensions:

1. Loosen the locking screws (4) , remove the locking cover (5) and the ball camera (3).

2. Attach the mounting base (1) to the wall or ceiling, wherever you want to install the camera. Locate a wall stud or ceiling joint and secure the base by the supplied screws (2).

3. Reinstall the ball and the locking cover.

4. Connect the 4 pin din to 12VDC and video output as below:

6. When picture shows up on the monitor, make the ball camera to the suitable position by rotating ball and locking cover.

7. Fix the ball camera by the locking screw.

Remark: please add the attached rubber ring on the rubber plate when the camera is set to 0-10 degree using.

Specifications:

| Model | AL-Mini01-700 |
| --- | --- |
| Optical Format | NextChip2040E + Sony 638 CCD |
| TV System | NTSC/PAL |
| Effective Pixel Array | 768 (H) x 494 (V) |
| Horizontal Resolution | 700TVL |
| Sensitivity | 0 Lux (LED On) |
| Scanning System | 625TVL/2:1 Interlace |
| Synchronization | Internal |
| Infrared Spectrum | 850 nm |
| IR LED | 12 LEDs |
| Infrared Range | 3m |
| Auto Gain Control | Auto |
| White Balance | Auto |
| Electronic Shutter | Auto |
| BLC | Auto |
| Video Output | 1 Vp-p, 75Ωcomposite |
| Lens | Standard f2.8mm fixed lens |
| View of Angle (D) | 120 degree |
| Pan Adjusting | +/-180 degree |
| Tilt Adjusting | 0-90 degree |
| Power Supply | 12V DC ±10% |
| Power Consumption | 180mA |
| Dimensions (ø X H) | 59 x 52 mm |
| Net Weight | 130 g |
| Weatherproof | IP67 |
| Operating Temperature | -20°C to +60°C |

*Specifications are subject to change without prior notice.

# Text boxes

1/3” Colour Mini Eyeball Camera