Model:AL-P08                                                          700T / 1080P, 12VDC, f3.6

Features:

● Outdoor vandal-resistant: IP67

● Max video resolution:  700TVL or 1920 X 1080

● Fixed focal megapixel lens, angle of view:  92° (D)

● Min illumination (color): 0.08 lux

● Megapixel sensor: 1/2.5”Aptina

● Mounting: Wall or ceiling

● Memory card slot: Option

● POE supply: support.

● Onvif support

● e-PTZ control: support

● Analog video output:l: Option

Packing list and dimensions:

Camera	      1

Instruction Manual	      1

Mounting Screw	      3

Mounting Plug               3

Specifications:

| Model | AL-P08 |
| --- | --- |
| Resolution | 1920*1080, 15FPS |
| TV System | PAL/NTSC |
| Image Sensor | 1/2.5”Aptina MT9P006 500 megapixel |
| Pixel | 1920*1080 |
| Illumination | Color 0.6/Black and white 0.08 Lux@F1.2 |
| Video Format | H.264 MP |
| Lens | f3.6 megapixel lens with fixed iris |
| Dual Streaming | Main streaming:1920*1080 |
|  | Sub-streaming: 704*576/352*288 |
| Video Bit Rate | 0.1M～12 Mpbs Adjusting |
| Protocol | HTTP, DDNS, DHCP, PPPoE, RTSP, RTP, RTCP, ONVIF |
| Rear Connection | HVR/NVR（Support HIK Vision’s and DaHua’s NVR） |
| Analog Video | Optional |
| Audio Processing | optional |
| Ethernet | 1 RJ45 Ethernet interface, 10/100 M adaptive, compatible with RTSP/FTP/PPPOE/DHCP/ |
| Wifi | --- |
| Power | DC-12V 1A |
| POE | Optional |
| SD Card | Optional |
| Alarm Input/Output | Optional |
| PTZ(RS-485) | Optional |
| Power Consumption | Max 3W |
| Dimensions | 111.0L x 103.8W x 51.8H |
| Net Weight | 600g |
| Running Environment | Temperature-20 ~ + 50 ° C, humidity 20 to 80% |
| Storage Environment | Temperature-20 ~ + 65 ° C, humidity 20 to 95% |
| Application Software | Bundled with CMS platform network management software and compatible I.E. browse; Meet Onvif standard; And support the iPhone/iPAD, Android |

AL-P08 Rev.A