Model:	AL-Mini02

##### High resolution,700TVL, 12VDC

Features:

●  Metal mini dome housing with standard fixed lens.

●  Available in black finish.

●  Low power consumption.

●  Easy installation on ceiling or wall, surface or flush mount.

●  High image quality and high low light performance.

Cautions:

- Please do not touch the glass with your fingers.  If necessary, use a soft cloth moistened with alcohol to wipe away the dust.

- Please avoid placing or using the camera under direct sunlight,

- Please ensure that the input voltage range is within the specifications.

- Do not attempt to service the camera by yourself. Please refer all services to qualified dealers.

Packing list:

Camera                       1

Instruction Manual	1

Mounting Screw	3

Option Lens        selectable from f2.1mm to f12mm

Operation procedures:

1. Remove the mounting base (1) by rotating anti-clockwise the locking cover (4).

2. Attach the mounting base (1) to the wall or ceiling, wherever you want to install the camera. Locate a wall stud or ceiling joint and secure the base by the supplied screws (5).

3. When picture shows up on the monitor, adjust the lens to obtain the best picture if is required, make the ball camera (2) to the suitable position by rotating ball (2) and middle cover (3).

4. Fix the ball camera by rotating clockwise locking cover (4).

Specifications:

| Model | AL-Mini02 |
| --- | --- |
| Pick up Device | Next Chip 2090 + 1/3” Sony 811 |
| TV System | PAL |
| Picture Elements | 796Hx 582V |
| Horizontal Resolution | 700TVL |
| Sensitivity | 0 Lux at F1.2 (Infrared LED On) |
| Scanning System | 625TVL |
|  | 2:1 Interlace |
| Synchronization | Internal |
| Infrared Spectrum | 850nm |
| S/N Ratio | More than 50 dB, (AGC Off) |
| Auto Gain Control (AGC) | Auto |
| White Balance | Auto |
| Electronic Shutter | Auto |
| BLC | Auto |
| Infrared LED | 12 |
| Infrared LED Range | 5m |
| Video Output | 1 Vp-p, 4Pin Din*1 |
| Audio Output | N/A |
| Mirror | N/A |
| Gamma Ratio | 0.45 |
| Auto-iris Lens Control | N/A |
| Lens | F2.1mm/2.8mm/3.6mm Standard Lens |
| Lens Mount | M12XP0.5mm Thread |
| Pan Adjusting | 0-360° |
| Tilt Adjusting | 0-45° |
| Power Supply | 12V DC ±10%, 4Pin Din*1 |
| Power Consumption | 330mA |
| Dimensions (ø X H) | 54 x43.4mm |
| Net Weight | 370g |
| Weatherproof/Water Proof | IP66 |
| Operating Temperature | -25°C to +65°C |

*Specifications are subject to change without prior notice.

REV. A

# Text boxes

1/3” Colour Dome Camera