Model: AL-MD5B

##### High resolution, 800TVL, 12VDC,180 view angle with Fish-eye Lens

Features:

●  Metal-cased IP67 weatherproof micro dome with fixed lens.

●  Lens Distortion Correction(LDC) against

●  Easy installation on ceiling or wall, surface or flush mount.

●  Including 0° 15°25°angled surface mount adapters.

Dimensions:

Use the attached hex key to loosen the hex head screw, then unscrew the top cover ~ if this is tight.

- Attach the mounting base to wall or ceiling, as required. Use the supplied screws to fix camera in position.

- Apply pressure to poly carbonate dome, and then move the ball to make the camera to the suitable position

- Connect the camera as follows:

12VDC power input and Video output to 4 din jack.

- Replace the transparent cover and the top cover.

- Re-tighten the hex-head screw to lock the dome camera.

Packing list:

Camera	              1

Instruction manual	              1

Hex-key                            1

Mounting screw	              4

Cable Connection:

Specifications:

| Model | AL-MD5B |
| --- | --- |
| Pick up Device | CMOS A139 |
| TV System | PAL |
| Effective Pixel Array | 976 x 582 Pixel |
| Horizontal Resolution | 800TVL |
| Sensitivity | 1 Lux (LED On) |
| Scanning System | 2:1 Interlace |
| Synchronization | Internal |
| Infrared Spectrum | N/A |
| Infrared LED | N/A |
| IR range | N/A |
| S/N Ratio | More Than 120 dB, (AGC Off) |
| Audio | Option |
| Auto Gain Control | Auto |
| White Balance | Auto |
| Electronic Shutter | Auto |
| Back Light Compensation | Auto |
| Video Output | 1 VP-p, 75Ωcomposite 4pin Din |
| Gamma Ratio | 0.45 |
| Lens | F1.8mm fish-eye lens |
| Horizontal angle of view | 180° |
| Pan Adjusting | N/A |
| Tilt Adjusting | N/A |
| Power Supply | 12V DC ±10% |
| Power Consumption | 70mA |
| Dimensions (ø X H) | 74.6 x 58.3 mm |
| Net Weight | 200 g |
| Weatherproof | IP67 |
| Operating Temperature | -25°C to +65°C |

*Specifications are subject to change without prior notice.

● Input voltage exceeding the nominal rating by over +/-10% will cause abnormal operation.

# Text boxes

180° Wide-angle Rear View Camera