Model:	AL-SV3-700

##### High resolution, 700 TVL, 12VDC, PAL

Features:

●  Metal-cased mini housing with standard fixed lens.

●  Available in gray finish.

●  Low power consumption.

●  Option 12 LEDs.

●  Easy installation on ceiling or wall, surface or flush mount.

Cautions:

- Please do not touch the glass. If necessary, use a soft cloth moistened with alcohol to wipe away the dust.

- Please avoid placing or using the camera under direct sunlight.

- Please ensure that the input voltage range is within the specifications.

- Do not attempt to service the camera by yourself. Please refer all services to qualified Dealers.

Packing list:

Camera	                  1

Instruction Manual	                  1

Mounting Screw	                  3

Optional Lens        selectable from f2.8mm to f12mm

Operation procedures:

Dimensions:

1. Loosen the locking screws (5) if is required, remove the mounting base (1) by rotating clockwise the locking cover (4).

2. Attach the mounting base (1) to the wall or ceiling, wherever you want to install the camera. Locate a wall stud or ceiling joint and secure the base by the supplied screws (6).

3. When picture shows up on the monitor, adjust the lens to obtain the best picture if require, make the ball camera (2) to the suitable position by rotating ball (2) and middle cover (3).

4. Fix the ball camera by rotating anti-clockwise locking cover (4) then lock the screw (5).

Specifications:

| Model | AL-SV3-700 |
| --- | --- |
| Optical Format | 1/3” Sony 811 CCD+NC2090 |
| TV System | PAL |
| Effective Pixel Array | 752 (H) x 582 (V) |
| Horizontal Resolution | 700TVL |
| Sensitivity | 4 Lux |
| Scanning System | 625TVL/2:1 Interlace |
| Synchronization | Internal |
| Infrared Spectrum | N/A |
| IR LED | Option |
| Infrared Range | 3m |
| Auto Gain Control | Auto |
| White Balance | Auto |
| Electronic Shutter | Auto |
| BLC | Auto |
| Video Output | 1 Vp-p, 75Ωcomposite |
| Audio Output | Optional |
| Lens | Standard f3.6mm fixed lens |
| View of Angle (D) | 90 degree |
| Pan Adjusting | +/-180 degree |
| Tilt Adjusting | 0-90 degree |
| Power Supply | 12V DC ±10% |
| Power Consumption | 130 mA |
| Dimensions (ø X H) | 68.8 x 59.2 mm |
| Net Weight | 180 g |
| Weatherproof | N/A |
| Operating Temperature | -20°C to +70°C |

*Specifications are subject to change without prior notice.

REV. A

# Text boxes

1/3” Colour Mini Eyeball Camera