You can choose the style

2.4GHz Wireless Transmitter  Camera    (DF-8073W)
Image Type: 1/3 Colorsony CCD
Resolution(pixels): PAL:500(H)*582(V) ,NTSC:510(H)*492(V)
Transmission Power： 10mW/CE 2mW/FCC
Estimate of 100 meter wireless send distance without block
Color System:PAL/NTSC
Vided Input : 1.0Vp-p 75 ohm
Shockproof: 10G
Waterproof: IP66

Free Operating Voltage: DC11-32 Volts
Dimensions: 71(W) x 51(H) x 48(D) mm (without mounting)
Weight Approx: 250g

2.4GHz Wireless Receiver 
Built in 4 CH(2.414/2.432/2.450/2.468)GHz Wireless Receiving
Receiving Sensitivity： ≤-80dBm
Color System:PAL/NTSC
Vided Output: 1.0Vp-p 75 ohm
Operating temperature: -20℃ to +50℃
Storage temperature: -30℃ to +80℃
Power suply: DC12V

External dimensions:L*W*T(38X28X18)mm 
Weight Approx: 50g
Product Accessories
User Manual