Model:	AL-MS01-700

##### Standard resolution, 700 TVL, 12VDC

Features:

●  Metal-cased mobile side view with fixed lens.

●  Available in silver finish.

●  Low power consumption.

●  Easy installation on ceiling or wall, surface or flush mount.

●  IP67 waterproof.

Packing list:

Camera	                  1

Instruction Manual	                  1

Self Drilling Screw	                  3

Hex Key                                1

Optional Lens        selectable from f2.8mm to f12mm

Dimensions:

Camera Module Orientation Matches Letter Orientation Illustrated:

(The front picture shown A orientation)

Operation procedures:

1. Loosen the lock screws (3) by applied hex key, remove the mounting base (2) from the camera (1).

2. Attach the mounting base (1) to the wall or ceiling, wherever you want to install the camera. Locate a wall stud or ceiling joint and secure the base by the supplied mounting screws (4).

3. Fix the camera on the mounting plate.

4. Connect the 4-pin din jack as the below diagram.

Specifications:

| Model | AL-MS01-700 |
| --- | --- |
| Pick up Device | Next Chip 2090 + 1/3” SONY 811CCD |
| TV System | PAL |
| Picture Elements | 796Hx 582V |
| Horizontal Resolution | 700TVL |
| Sensitivity | 0 Lux at F1.2 (Infrared LED On) |
| Scanning System | 625TVL |
|  | 2:1 Interlace |
| Synchronization | Internal |
| Infrared Spectrum | 850nm |
| S/N Ratio | More than 50 dB, (AGC Off) |
| Auto Gain Control (AGC) | Auto |
| White Balance | Auto |
| Electronic Shutter | Auto |
| Back Light Compensation | Auto |
| Infrared LED | 12 LEDs |
| Infrared LED Range | 8m |
| Video Output | 1 Vp-p, 75Ωcomposite , 4 Pin Din |
| Audio Output | Option |
| Mirror | N/A |
| Gamma Ratio | 0.45 |
| Lens | F3.6mm Standard Lens |
| Exterior Focus Adjustment | N/A |
| Lens Mount | M12XP0.5mm Thread |
| Pan Adjusting | 0-360° |
| Tilt Adjusting | 0-40° |
| Power Supply | 12V DC ±10% |
| Power Consumption | 190mA |
| Dimensions (L X W X H) | 76.4 x 60.5 x 56mm |
| Net Weight | 215g |
| Weatherproof/Water Proof | IP67 |
| Operating Temperature | -25°C to +55°C |

*Specifications are subject to change without prior notice.

# Text boxes

1/3” DSP Colour Mobile Side View Camera