Model:	AL-MB01-600

##### High resolution, 600TVL, 12VDC

Features:

●  Metal-cased with fixed lens.

●  Available in black or silver

●  Low power consumption.

●  IP68

●  8.5-18VDC power input

Packing list:

Camera	                  1

Instruction Manual	                  1

Optional Lens        selectable from f2.1mm to f6.0mm

Operation procedures:

1. Loosen the locking ring, remove the camera to the suitable position.

2. Fix the camera by the locking ring.

3. Connect aviation head  to video output to lead cables.

Connection:

Specifications:

| Model | AL-MB01-600 |
| --- | --- |
| Pick up Device | NextChip 1089+1/3” Sony 811 CCD |
| TV System | PAL |
| Picture Elements | 976H x 582V |
| Horizontal Resolution | 600 TVL |
| Sensitivity | 0 Lux (LED On) |
| Scanning System | 625TVL/2:1 Interlace |
| Synchronization | Internal |
| Infrared Spectrum | 850nm (day/night version) |
| Infrared LED | Non |
| S/N Ratio | 50 dB |
| Auto Gain Control | Auto |
| White Balance | Auto |
| Electronic Shutter | Auto |
| Back Light Compensation | Auto |
| Mirror | Non |
| Audio | N/A |
| Video Output | 1 Vp-p, aviation head Jack |
| Gamma Ratio | 0.45 |
| Lens | F2.1mm lens |
| Field of View (D) | 145 degree |
| Power Supply | 8.5-18V DC DC Jack |
| Power Consumption | 130mA |
| Dimensions (ø X H) | 29*25*23MM |
| Net Weight | 110g |
| Weatherproof | IP68 |
| Operating Temperature | -30°C to +80°C |

*Specifications are subject to change without prior notice.

# Text boxes

1/3” CCD Colour Bumper Camera